APM Customer Experience  Transaction Definition Recording Mechanisms

Version 0.3 November 5, 2011

Hallett German

Sr. Support Engineer

CA Technologies, Inc.

Hallett.German@ca.com

Table of Contents

- Introduction

- Guiding Principles

- Comparison of Five Recording Approaches

- Etcetera

Introduction

This document covers the five ways to record and create APM Customer Experience transactions.

Guiding Principles

- Each approach is a tradeoff between recording speed, post-transaction definition cleanup time, and transaction granularity. Use the approach that makes sense for the transaction.

- Future CEM releases could add these enhancements:

  - Add the capability to record additional types of transactions (such as Web 2.0/Web 3.0)

  - Add wizards to help determine the user and session identifier for an application.

  - Add wizards to make suggestions on transaction definition configuration.

  - Add tools to help debug recording issues.

  - Better handle XML and Web Services.

  - Ability to merge and move recordings across recording sessions.

Comparison of Five Recording Approaches

| Approach | Pros | Cons | When to Use |
| --- | --- | --- | --- |
| AutoDiscovery (Built-in APM 9 and later) | Built into CEM Easily capture transactions. | Not meant for continuous use Not able to import XML from transaction definitions. Only able to capture transactions. | To monitor new definitions When capturing many transactions quickly. When do not have assistance of application staff. |
| Advanced Recorder | Ease of use Built into CEM Administrator. Can cleanup definition before promoting. Can run on any client browser. Can capture entire business transaction. | Getting valid definitions for a large number of transactions may be time consuming. | When capturing Business Transactions is important. XML and Web Services |
| Manual Transaction Definition Creation (No Recording) | Built into CEM Administrator Console Ease of use Can capture entire business transaction. | Transaction definition will not usually include all components. | When transaction is just a few URLs. |
| Script Recorder | Built into CEM Works with Load Runner logs or Ethereal/Wire Shark Scripts | Unable to import scripts directly which knows when a business transaction starts and stops, Post transaction definition cleanup may take time. A command line interface may be prone to user error. Runs on MS Windows only. May be unable to import large scripts. | Bulk recording Transaction is available only as a LoadRunner logs or as Ethereal/ WireShark scripts. HTTP is in TCP packet. Client-less applications (need to capture traffic from application server) |
| WTG (Wily Transaction Generator) | Ease of use Can be used to create definitions for synthetic or actual transactions. | Requires WTG to be operational Post transaction definition cleanup may take time | Bulk Recording Web Services XML and Web Services |

Etcetera

Credits and Acknowledgements

WTG Implementation Guide

APM Transaction Definition Guide