TIM Success Guide: Part 1: Overview

[Setting Up and Validating a TIM Network Connection & TIM Health -- for software and MTP TIMs.]

3.0f 7-12-16 Preview Draft – Comments Appreciated

Hallett German

Senior Support Engineer

CA Technologies, Inc.

Hallett.German@ca.com

Table of Contents

- What’s Changed.

- Introduction

- Out of Scope

- Keys for Successful TIM Monitoring & Recording

- Tools to Use?

- Appendices

- Etcetera

1. What’s Changed.

Back in 2011, the TIM Readiness Guide 1.x was created to help CA staff and customers to simply determine if their connection from the switch to the TIM was correctly implemented. The last update of the Guide (2.1) was in 2013 when MTP and other content was added.

Since the original document’s creation, there has been the following technological and product changes:

- The transformation of the SSL protocol into TLS.

- The improvements in TLS 1.1 & 1.2.

- A dramatic rise in the volume and complexity of network traffic.

- An increase in the complexity of networks and their corresponding hardware.

- More options in the numerous ways that a TIM can capture traffic from a switch.

- An expansion of CEM and APM functionality in APM 9.x and later.

- Higher customer expectations on what a stable and successful TIM means.

- Less staff and more aggressive deadlines to rollout monitoring new applications.

This means that there is a need to document a lot more than getting a TIM implementation-ready. There is a need to focus also on periodically optimizing and maintaining TIMs than what was done in the past.

Hence the new name and focus of this guide which is broken into three parts:

Part 1: Overview (This Document)

- Introduce why the need for the new document.

- Explain common problems and causes.

- Discuss Keys for TIM Success

- Review common troubleshooting tools

Part 2: Best Practices

- Optimizing and Maintaining

Part 3: Troubleshooting TIM Issues

- Reviews high-level checklist

- Overview of TIM Issues

2. Introduction

The types of TIMs (Appliance, Timsoft, MTP, High Performance TIM) have changed over the years. These various TIM types combined with the trends mentioned in the previous section can lead to a wide variety of TIM problems.

Common issues are listed below:

- Not seeing any Network traffic.

- Not seeing Network traffic from a particular Subnets)/IP address(es).

- Unable to Record.

- Unable to Decode SSL traffic.

- High CPU/Memory

- Frequent TIM Restarts.

- High Dropped Packets.

- High OOO Packets.

- TIM Crashes

- TIM seeing far less or much more transactions than a comparable system.

Common causes include:

- Troublesome custom HTTP Plugins.

- Invalid SSL private keys or passphrases.

- SSL cipher suites or TLS version used

- Sending more traffic to the TIM that it can handle.

- Monitoring far too many transactions.

- Invalid TIM/MTP configuration settings.

- MTP Hardware Filters or AP CE (CEM) Web Server Filters.

- Traffic Quality issues.

- Span/Tap/Aggregator settings.

Most of these solutions are documented in hundreds of KDs (Knowledge Documents), Tech Tips, and other locations. Still, new issues arise and old issues persist.

This guide attempts to provide a framework for

- Making the needed changes to avoid scenarios that may impact the TIM successfully processing transactions.

- TIM Optimization and Maintenance Best Practices.

- First steps on what to do should TIM issues arise.

The goals of this document are

- Help you maintain/optimize a stable and scalable TIM.

- Reviewing avoidable problems and their possible resolution. Failure to do this results in instability or creating false positives. The result may have a negative impact on TIM performance.

3. Out of Scope

The following topics are out of scope for this document:

- APM architecture review.

- APM internals review.

- TIM installation, upgrade, or migration steps.

- APM Database/EM Performance issues and logs.

- Comparing and contrasting network connection types (such as Span port vs. network tap.)

- A general APM Customer Experience and networking tutorial including troubleshooting.

- General network data integrity troubleshooting

- Networking overview

- Tutorial for tools such as tcpdump, ssldump, wireshark, and more.

4. Keys for Successful TIM Monitoring & Recording

[Note: Feel free to copy any of the following tables for a “Tim Healthcheck document” to assess the performance of a new or existing TIM.]

A TIM will only be able to successfully record and monitor transactions if it can

do reliably the following tasks.

| Activity | Pass | Fail | Notes |
| --- | --- | --- | --- |
| Successfully capture a client roundtrip HTTP or HTTPS client session. |  |  | Assumes there is path affinity (i.e. the session always come back to the same load balancer/web server). Depending on TIM placement, it may only be a roundtrip from the client to the load balancer or firewall. |
| Seeing both HTTP/HTTPS requests and responses |  |  | This includes GETs, POSTs, and HTTP Status Codes. |
| Seeing TLS requests and responses |  |  | This includes Server/Client Hellos, Client Keys Exchanged, Application data, SSL Alerts, and more. |
| The Application is using a TLS Ciphersuite that TIM knows how to decode. |  |  | For example, not Diffie-Hellman. See Supported Ciphersuites. |
| Seeing two-way traffic from the specific web servers/load balancers/firewalls/etc. |  |  | This may be virtual or physical addresses. |
| TIM is not dropping packets |  |  | This is usually due to the switch network connection providing more traffic than the TIM can handle. |
| The switch connection is not overloading TIM with unnecessary traffic. |  |  | Unneeded traffic for TIM to monitor includes DNS, router, or SMTP requests and responses. |
| Complete HTTP Headers |  |  |  |
| Seeing a minimum number of out of order packets |  |  |  |
| The business transaction taking longer than TIM Setting for connect timeouts (ConnectionTimeoutInSeconds.) |  |  | . |
| Adequate capture buffer size. |  |  | In 10.1/10.2 , the CaptureBuffer size has not be changed from the default which will also be another reason for dropped packets |

A  TIM is healthy and responsive which means the following:

| Activity | Pass | Fail | Comments |
| --- | --- | --- | --- |
| The number of restarts and crashes are kept to a minimum. |  |  |  |
| TIM CPU and memory do not approach or exceed capacity limits |  |  |  |
| The MTP/TIM Ram disk does not overfill. |  |  |  |
| TIM successfully processes the defect, stats, and other files in the “data/out” directories. This also means no files backed on the TIM, no files being corrupted, or of zero length. |  |  |  |
| TIM can successfully handle peak and short-term increased capacity processing. |  |  |  |

Ultimately it is a customer responsibility to have a healthy and optimal TIM.  This is not just a one-time but an ongoing event. This includes the following periodic tasks for each TIM to ensure smooth operations:

| Task | Frequency | Comments |
| --- | --- | --- |
| Check operating system viability | After installs and upgrades or quarterly | Impact on upgrades of operating system, drivers, and third party applications on TIM performance/stability. |
| Check TIM switch connection is seeing all appropriate traffic from all monitored applications. | Monthly | So the core switches/firewalls/load balancers, spans, network taps, and aggregators are not filtering out desired traffic. |
| Check that TIM switch connection is having minimal network data quality issues. | Monthly | The TIM is not seeing dropped packet, out of order packets, and seeing the roundtrip of the TCP conversation. Use pcap analysis to verify this. |
| Check that TIM switch connection is seeing two-way and not truncated HTTP, HTTPS, and Flex traffic | Monthly | Use pcap analysis and TIM logs to show this, |
| Check that usernames/real customer IPs are being retained throughout the transaction. | Quarterly | May need to use X-Forwarded-For, True-Client-IP and equivalent headers to configure in the ProxyForwardHeader TIM Setting |
| Check all ports are open in the appropriate directions | Quarterly | See Open APM Ports for more details. |
| Check that a transaction is handled correctly through a reverse proxy, firewall, load balancer, etc. | Quarterly | Use pcap analysis and analyze logs on these devices, |
| Check that the private keys are correctly imported into the TESS/TIM. | After import | Use openssl, TIM logs, and wireshark to verify. Also see if there are passphrase errors. |
| Check that private key/certificate has not expired | Monthly | Look at certificate expiration date |
| Check that application(s) support TLS versions, ciphersuites etc | Quarterly or after adding new web servers | Look at pcap or HTTP Session for this information. |
| Check that a synthetic transaction generator or load tester used can generate HTTP/HTTPS packets with the correct text/html (or equivalent) content type. | Quarterly or after adding new web servers | Look at pcap, TIM logs, or HTTP Session for this information |

Notes:

- There could other factors impacting TIM that this approach cannot

determine. For those, a support case may be needed.

- If a multi-port card is being used in the TIM or MTP (such as Napatech), ensure that all ports are working as expected with the network connections.

5. Tools to Use?

To keep TIM healthy, there are a variety of tools that can be used

- To collect log files and packet captures from the TIM.

- To monitor TIM Health

- To analyze packet captures from the TIM

There are four questions that need to be answered to validate the overall TIM network setup:

1. Are we seeing traffic?

2. What is the quality of the network traffic?

3. Are we seeing valid and two-way HTTP traffic?

4. Are we seeing valid and two-way HTTPS (SSL) traffic?

| Tool | What is it used for? | MTP or TIM | Link |
| --- | --- | --- | --- |
| Buildcap | To collect a pcap | MTP only | Installed on mtp /opt/NetQoS/bin/buildpcap --help Support will provide further directions as needed |
| Ssldump | To analyze SSL traffic | MTP & TIM | SSLdump link |
| tcpdump | To collect a pcap or show TCP and HTTP traffic | MTP & TIM | Installed on mtp/tim -- TCPdump manual |
| Wireshark | To analyze packet captures | Runs on desktop unless using tshark | Download Wireshark |
| Monit | Monitor TIM | MTP or TIM | Contact Jorge Mertin directly. This is supported AS-IS. |
| TIM Field Pack | Monitor TIM | MTP or TIM | An older version is here. Contact Support for a current copy. This is supported AS-IS. |

12. Etcetera

Credits & Acknowledgements

(To be added) My thanks to xxx for reviewing